## Slide 1: CSED311 Lab2: RTL Design
Jaehun Ryu
jaehunryu@postech.ac.kr
Contact the TAs at csed311-ta@postech.ac.kr

## Slide 2: Contents
Combinational logic
Register-Transfer Level
Finite State Machine
Assignment

## Slide 3: Combinational logic
Represents Boolean function (time(clk)-independent)
Output is a function of inputs only
output = f(input)
Example: 4-to-1 mux

## Slide 4: Combinational logic
Implementation with Verilog (mux)
Using Assign | Using Always

## Slide 5: Combinational logic
RTL schematic

## Slide 6: Register-Transfer Level
The design method to implement a synchronous circuit with a HDL (Hardware Description Language)
Synchronous circuit consists of:
  Register: a memory element synchronized by the clock signal
  Combinational logic: logical function

## Slide 7: RTL - example
Toggler example
<Fig 1. “Register transfer level - example toggler” (Register-transfer level, Wikipedia, https://en.wikipedia.org/wiki/Register-transfer_level)>

## Slide 8: RTL - example
Toggler example

## Slide 9: Finite State Machine (FSM)
Moore machine
Mealy Machine

## Slide 10: Finite State Machine (FSM)
Moore Machine
  Outputs only depend on the current state.
Combinational Logic
REGISTER
(state memory)
Combinational Logic
INPUT
OUTPUT
STATE
STATE
clk
OUTPUT only depends on STATE
-> OUTPUT changes at clk only
(synchronous)

## Slide 11: Finite State Machine (FSM)
Mealy Machine
  Outputs depend on the current state and the current inputs
Combinational Logic
REGISTER
(state memory)
Combinational Logic
INPUT
OUTPUT
STATE
STATE
clk
OUTPUT depends on STATE and INPUT
-> OUTPUT can be changed when INPUT changes, even no clk (asynchronous)

## Slide 12: Finite State Machine (FSM)
Mealy Machine
  Mealy Machine can be made synchronous
Combinational Logic
REGISTER
(state memory)
Combinational Logic
INPUT
OUTPUT
STATE
STATE
clk
D flip flop

## Slide 13: FSM Code Structure
ports and variables declaration
Combinational logic
Sequential logic
Combinational logic derives the next state and outputs
assign statement + wire data type
always @(…) block + reg data type (assignment)
Sequential logic stores the current state
always @(posedge clock) block + reg data type (assignment)

## Slide 14: FSM Code Structure
z is output and z is in combinational logic part
-> asynchronous Mealy Machine

## Slide 15: FSM Code Structure

## Slide 16: Assignment
Implement a simple vending machine RTL in Verilog
  A simple Finite State Machine (FSM)
Your vending machine should cover all use-cases (in the next slides)
A skeleton code and testbench will be provided.
Submit a report and code to LMS
  Due date
    Code: 2021. 3.15 / 09:00 am
    Report: 2021. 3. 15 / 24:00 am
  Demo
    2021 3. 16 07:30 pm ~ 09:30 pm

## Slide 17: Assignment
Vending machine interface
INPUT |  | 
Signal | Description | Number of bit(s)
i_input_coin | Insert Coin | 1 for each type of coins
i_select_item | Select Item | 1 for each type of items
i_return_trigger | Return change | 1
clk | clock | 1
reset_n | reset | 1
OUTPUT |  | 
Signal | Description | Number of bit(s)
o_output_item | Indicate dispensed items | 1 for each type of items
o_available_item | Indicate item availability | 1 for each type of item
o_return_coin | Indicate type of coin (change) | 1 for each type of coins

## Slide 18: Assignment
Vending machine use-case
Assumption: infinite item, change
Sequence
1. Insert money (available money unit: 100, 500, 1000 won) and initialize waiting time(=100)
2. Vending machine shows all available items where (item cost <= current money)
2.a. decrease waiting time(-1)
3.a. Insert money within the waiting time
3.a.1. Go to 2 and initialize waiting time(=100)
3.b. Select an item within the waiting time
3.b.a. Case1: the item is available
3.b.a.1. The item is dispensed
3.b.a.2. Go to 2 and initialize waiting time(=100)
3.b.b. Case 2: the item is unavailable
3.b.b.1. Nothing happens. Waiting time is not reset.
3.c. No input within the waiting time
3.c.1 Return changes
a*. Whenever press the return button
a*.1. Return changes
a*.2. Go to 1

## Slide 19: Assignment
Submission
  Submit your assignment to LMS with filename:
    Lab2_{TeamID}_{StudentID1}_{StudentID2}.pdf
      PDF file of your report
    Lab2_{TeamID}_{StudentID1}_{StudentID2}.zip
      Zip file of your code (*.v)(without testbench)

## Slide 20: Assignment tips
If your modelsim is not displaying the output of $display or $monitor, then try using vending_machine_tb_f.v. (output will be written to output.txt)
If your simulation keeps running, the testbench module is waiting for the output signals. (o_output_item or o_return_coin)
If your vending machine code passes all tests, you will get the message “Passed = 23, Failed = 0”.

## Slide 21: Assignment tips
#1: When modeling sequential logic, use nonblocking assignments.
#2: When modeling latches, use nonblocking assignments.
#3: When modeling combinational logic with an always block, use blocking assignments.
#4: Do not mix blocking and nonblocking assignments in the same always block.
#5: Do not make assignments to the same variable from more than one always block.
#6: Use $strobe to display values that have been assigned using nonblocking assignments.
#7: Do not make assignments using #0 delays.

## Slide 22: Evaluation criteria (source code)
ModelSim 동작여부
ALL PASS 여부
전체적인 기능 이해 여부
FSM의 이해 여부
모듈화 여부
Combinational logic의 이해 여부
Sequential logic의 이해 여부

## Slide 23: Announcement
If you have any problem, contact TAs with following options
  Microsoft Teams – Lab QnA channel (highly recommended)
  Mail – TA alias (“csed311-ta”)
  PLMS – Question Board
Please check the new team number and time slot in PLMS
A time slot will be open in 2021-03-09 22:00:00

## Slide 24: Reference
“Register-transfer level”, Wikipedia, last modified Jan 24, 2019, accessed Mar 03, 2019, https://en.wikipedia.org/wiki/Register-transfer_level
http://www.sunburst-design.com/papers/CummingsSNUG2000SJ_NBA.pdf